Environmental Control System
# Introduction

# Method
## Mass Processing
1. We assume an atmosphere A, moving from state A1 to state A2. We also use an ideal model of atmosphere A called I, which is at the target temperature and pressure. During each loop, the values of A should move closer to I.
2. We define functions O(P) and I(P), which give volumetric transfer rates in m^3/s at a specified pressure. O and P are mirrored across PI, the pressure of atmosphere I. As P increases, O(P) decreases while I(P) increases.
3. bar x_i = left[stack{1-x_Oi#x_Oi#0#dotsvert}right], ~R_i = R(x_i)
4. bar M_i = {bar x_i P_i V_A} over {T_i R_i}
5. bar dm_i = bar M_i over V_A O(P_A)dt
6. bar dm_A = bar M_A1 over V_A I(P_A)dt
7. Ensure that dm_A does not exceed M_A (It should never so long as I(P_A) is lower than V_A and dt is less than 1.
8. bar M_A2 = bar M_A1-bar dm_A
9. bar N = left[stack{bar dm_"A-N2"#0#0#dotsvert}right], ~bar O = left[stack{0#bar dm_"A-O2"#0#dotsvert}right], ~bar C = left[stack{0#0#bar dm_"A-CO2"#dotsvert}right], ~bar T = bar dm_A-(N+O+C)
10. Use gas in tanks to shift N, O, and C towards their ideal values.
11. bar M_A2 = (bar M_A1 - bar dm_A)+(bar N+bar O+bar C)
## Heat Processing
1. Same definitions as Mass Processing
2. Q_i = T_i C_p(bar x_i)
3. dQ_A = Q_A sum {bar dm_A over bar M_A}
4. dQ_i = Q_i sum{bar dm_i over bar M_i}
5. Q_A2 = (Q_A1-dQ_A)+dQ_i